PRODUCTS

MANUFACTURERS

Provide Megapixel IP camera with streaming video technology by one of the following manufacturers:

ACTi

Megapixel Camera

Provide ACTi Model E44A Megapixel camera with features and characteristics as follows:

Imaging

Image Sensor: Progressive Scan CMOS

Sensor Size: 1/2.8  inch

Effective Pixels: 1984(H) x 1225(V) (2.43 MP)

Horizontal Resolution (TV lines): 1100 TVL

S/N Ratio: 52 dB

Minimum Scene Illumination

Color: 0.1 Lux at F1.4 (2400 ºK, 30 IRE).

Black and White: 0 Lux (IR LED on).

IR Illuminators

IR Sensitivity Range: 700 – 1100 nm

Adaptive IR (IR Exposure Compensation) x 15 (850 nm)

IR Working Distance: 30m (0 Lux, 30 IRE, Max exposure gain)

Lens

Focal Length: Vari-focal, f2.8-12 mm

Aperture: F1.4

Iris: Fixed Iris

Focus: Manual focus

Lens Mount: Board Mount

Horizontal Viewing Angle: 92.5º - 35.9º

Day/ Night

Day/Night switching : ISP based switch, configurable

Mechanical IR Cut Filter: Yes

Electronic Shutter:

Manual Mode : 1/5 – 1/2,000 sec

Auto Mode : 1/5 – 1/10,000 sec

Functions

Superior Low Light Sensitivity (SLLS) : Automatic

Basic WDR (75 dB)

White Balance: Auto/ hold /manual.

Brightness

Contrast

Automatic Sharpness

Automatic Gain Control

Digital Noise Reduction

Flickerless

Image Orientation: Image Flip / Image Mirror

Privacy Masks: 4 configurable regions

Text Overlay: User defined text on video

On-Screen Graphics: User defined image layer on video

Calendar function with on-chip clock (Realtime clock)

Alarm:

15.1 Alarm Trigger:

Video motion detection: 3 motion regions

Sound detection

External device through digital input

15.2   Alarm Response:

a. Notify control center

b. Change camera settings

c. Command other devices

d. E-mail notification with snapshots

e. Save video or snapshot to local storage

f. Upload video, snapshot to FTP server

g. Activate external device through digital output

Video Analytics:

16.1 System requirement:

PC based Smart Search Tool, IVS Server or ALPR Server is required

16.2   Software Based Analytics:

a. Motion Detection

b. Line crossing

c. Enter Area

d. Missing Object

e. Unattended Object

f. Tamper

g. Object Counting

h. People Counting

i. License Plate Recognition

Compression: H.264 (Baseline/ Main/ High profile) / MJPEG.

Picture Resolution:

1920 x 1080

1280 x 720

800 x 600

640 x 480

320 x 240

Maximum Image Frame Rate:

30 fps at 1920 x 1080

30 fps at 1280 x 720

30 fps at 800 x 600

30 fps at 640 x 480

15 fps at 320 x 240

Bit Rate: 28k – 6Mbps per stream; Support Constant and Variable Bit Rate Mode.

Multi-Streaming: Simultaneous dual streams based on two configurations.

Audio

Audio: two-way

Compression: PCM 8 kHz, 16 bit encoding, mono; G.711 aLaw/uLaw

Audio Input: 1, cable with 3.5mm Phone Jack

Audio Output: 1, cable with 3.5mm Phone Jack

Interface:

External Button: Reset button for factory default setting

Local Storage: MicroSDHC/MicroSDXC memory card slot(card not included)

Digital Input:  1, cable without connector.

Digital Output: 1, cable without connector

Networking

Network Port: 1, Ethernet (10/100Base-T) via RJ-45 connector.

Protocol: TCP, UDP, HTTP, HTTPS, DHCP, PPPoE, RTP, RTSP, IPv4, IPv6, DNS, DDNS, NTP, ICMP, ARP, IGMP, SMTP, FTP, UPnP, SNMP, Bonjour, ONVIF Compliant.

Security: IP address filtering; HTTPS encryption; Password protected user levels; Anonymous login; IEEE 802.1X network access control.

Integration

Unified Solution : Fully compatible with ACTi software

ISV Integration: Software Development Kit(SDK) available ; ONVIF Compliant

GPS position by manual setting

Firmware Access Browser: Microsoft Internet Explorer 8.0 or newer (full functionality); Safari with QuickTime installed, and other browsers with VLC installed (partial functionality)

Environmental Casing

Weatherproof (IP68)

Vandal proof metal casing (IK10)

Mount Type:

Wall, Ceiling, Pole, Gang Box

Power Source / Consumption

PoE Class 2 (IEEE802.3af) / 5.76 W (IR LED on)

Physical Characteristics:

Dimensions (Ø x L): 77 mm x 291 mm (3.03” x 11.5”)

Weight: 1007g (2.22 lb)

Temperature

Starting Temperature: -20ºC - 50ºC (-4ºF - 122ºF)

Operating Temperature:-40ºC - 50ºC (-40ºF - 122ºF)

Operating Relative Humidity: 10% ~ 85% RH

Approvals:

CE (EN 55022 Class B, EN 55024), FCC (Part15 Subpart B Class B), IP68, IK10 (metal casing), UL (for optional PoE injector)

Warranty:

3 years

END OF SECTION